ELT 1010: Lesson 4

Practical Assignment

Name: __________________________________                              Date: _______________

Obtain the following items:  4 “A” size battery holders, 4 “A” size batteries, a single pole knife switch, 3 lamp holders, 3 1.5V lamps, 5 leads with alligator clips, and an analog multimeter.  Read the operating instructions for the multimeter before beginning this assignment.

1. Make sure that the leads in the multimeter are properly attached, then set the dial to 10V DC.

a. Touch the red lead to the positive end of one of your

batteries and the black lead to the negative end of the

battery. What does the scale read? ________. How does

this result compare with what is printed on the battery?

____________________________________________

b. Place two batteries end to end so that the positive of one

touches the negative of the other, use clip leads if needed.

Now measure the volts at the end of these two batteries.

What is your result? _________. Put 3 batteries together,

End to end in the same manner and measure the voltage.

The result is __________. Now put all four batteries

together and measure the voltage. __________

What can you say about the voltage of batteries linked

together in Series? ___________________________

___________________________________________

c. Put 2 batteries together in series. Connect a lead to the

negative end to one side of the knife switch. Connect another

lead from the other side of the switch to one side of a lamp

holder with a lamp in it, then connect the other side of the

lamp holder to the positive side of the battery pack. The

batteries are the source of _________, and it should be

_______V. Another term for the positive terminal of the

battery is the _________________ and another term for the

negative terminal is the ____________________. If the batteries

produce enough voltage to push current the lamp will light up

when the switch is closed. Did it? _________

d. Now take the multimeter, still set on 10V DC, and connect

the leads on each side of the knife switch and then the lamp.

What voltage reading did you get across the switch? ________,

the lamp? ________. If you add the two voltage drops together,

it should equal the source voltage, is this true in your case? _______

Add two more lamps to the system, if they don’t light you may

have to add another battery as well. Then measure the voltage drop

across the switch and across each lamp. They are; switch _______,

Lamp #1________, Lamp #2 _________, Lamp #3 ________

If you add up the 4 voltage drops does it equal the source voltage?

You have now proved Kirchoff’s Law of voltage in a series circuit; that the sum of the voltage drops across the components in a circuit are equal to the source voltage.

2. Current is the number of electrons passing a point in the circuit.

Current is measured in Amperes (Amps) or Milliamps for smaller

currents. In a series circuit there is only one path for the current

to flow, so the current is the same throughout the circuit.

Set your multimeter to its highest amp setting and then connect the

two leads directly to the switch and the lamp so the current must

flow through the meter. What happens to the needle? _________

____________________________________________________

If the needle jumps to the end of the scale immediately

disconnect it as the current is too high for the meter. If the needle

is in the middle of the scale then record your reading. If the needle

barely moves or doesn’t move at all you can set the meter to the next

lower scale until the reading is readable. What is the current in your

circuit? _________________

3. Resistance is the opposition to current flow. There is resistance in

every component including the wires. High resistance at a point in

a circuit could show a bad connection or a corroded contact. You

must not have the power on to measure the resistance across a

component. Resistance is measured in OHMs. Locate the ohms scale

on your multimeter, then select a higher ohm scale than you think you

might need just as you did for current measurements. Before you can

measure the reistance of a component you must Zero the needle by

holding the two test leads together and adjusting the ohms adjust knob

until the needle lines up with zero on the scale. Your ohmmeter is now

ready to use.

Now place the leads on either side of a component and measure the

ohms of resistance. If the needle doesn’t move then you can switch

to a lower resistance scale. What is the resistance across the following:

wire lead #1 _______________  Wire Lead #2 _______________

wire Lead #3_______________  Wire lead #4 ________________

closed knife switch _________________

Lamp #1 ____________ Lamp #2 ______________ Lamp #3 _________

If you added up all the resistances you would get the total resistance to

current in the series circuit., which is ________________.

4.  What test could you use to find a bad connection in a circuit that was on?

__________________________________________________________

You are now done the assignment. Put away all of your materials and supplies where they belong

_____out of 30 = _____%