ELT 1010: Lesson 5

Wire Repair

Practical Assignment

Name: _________________________________                                Date: _______________

Watch an appropriate YouTube video demonstrating proper soldering techniques.

Obtain #18 gauge multistrand wire and, using side cutters, cut 16 pieces 4 inches or 10 cm. long.  Use wire strippers to properly remove insulation from one end of each piece of wire (approx. ¾” – 2 cm).

Use these wires to make 2 good examples each of the three joining methods described in this lesson.  Then properly set up your soldering station and when ready properly solder the 6 joints you have made so that they are secure. Show the results to your instructor for grading.

Twisted Joint ___________         Parallel Joint ______________     Spread Joint ___________

Use a solderless ”Butt “connector  and crimping pliers to join two of the wires together then show it two your instructor. Redo the joint then use electrical tape to properly wrap the joint. You should now have two solderless joints one taped and one not.

Untaped  _____________                    Taped _____________

Take one each of the original 6 joints that you made and tape one, liquid tape the another and use shrink tube to seal and insulate the third. Have your instructor look at the results.

Taped Joint ___________    Liquid Taped joint __________     Shrink Tube ___________

_____ out of 8 = _____%